## Slide 1: Identifying Environmental Challenges of Chlor Alkali Industry
<number>
Expert Group Meeting (EGM) to identify barriers and opportunities for developing countries
27-28 June 2016
Vienna, Austria
Desirée Montecillo Narvaez
Programme Officer
Chemicals and Waste Branch
UNEP Division of Trade Industry and Economics

## Slide 2
<number>
Management of Sites Contaminated with Mercury Wastes
Complicated
Preliminary Assessment which identifies the nature and scope of contamination, including contamination by other toxic chemicals that may be present.
Site Investigation which identifies the area of contamination and assesses the surface and subsurface extent of contamination.
Feasibility Studies which determine what technical options are available to manage or remediate the site including evaluating how each alternative can best reduce or eliminate contamination from the side, and the cost of each option
Final Decision document which presents the best approach to managing or remediating the site.
Time consuming
costly effort.
Notes: Mercury contamination differs from other contaminants due to mercury’s unique behavior
Regardless of these concerns, it is suggested for governments to identify and inventory sites contaminated with mercury, ensure that the source of the contamination is contained to prevent any further contamination and remediate the site as soon as feasible to reduce exposure to humans and the environment
At contaminated sites the surface and sub-soil, sediment, surface and ground water may need to be adequately treated. A number of processes are available for on– and off-site treatment (see for example the EU‘s relevant Best Available Techniques Reference Document (BREFs)51 or the US EPA‘s ‘Treatment Technologies for Mercury in Soil, Waste and Water’80
<number>

## Slide 3
<number>
Each Party shall endeavour to develop appropriate strategies for identifying and assessing sites contaminated by mercury or mercury compounds.
Any actions to reduce the risks posed by such sites shall be performed in an environmentally sound manner incorporation, where appropriate, an assessment of the risks to human health and the environment from the mercury or mercury compounds they contain
Contaminated Sites under the Minamata Convention: Art. 12, Para 1 and 2
Article 12
Contaminated sites

## Slide 4
<number>
Contaminated Sites under the Minamata Convention: Art. 12, Para 3
Site identification and characterization
Engaging the public
Human health and environmental risk assessments
Options for managing the risks posed by contaminated sites
Evaluation of benefits and costs; and
Validation of outcomes
Parties encouraged to cooperate
3. The Conference of the Parties shall adopt guidance on managing contaminated sites that may include methods and approaches for:

## Slide 5
<number>
Identification of contaminated sites and emergency response
241. A mercury-contaminated site that poses a threat to human health or the environment can be identified through:
a. Records identifying past industrial or other activities at the site
b. Visual observation of the site conditions or attendant contaminant sources;
c. Visual observation of manufacturing or other operations known to have used or emitted a particularly hazardous contaminant;
d. Observed adverse effects in humans, flora, or fauna presumably caused by the proximity to the site;
e. Physical or analytical results showing contaminant levels; and
f. Reports from the community to the authorities of suspected releases.
Source: Basel Convention technical guidelines on the environmentally sound management of mercury waste, Conference of the Parties to the Basel Convention on the Control of Transboundary Movements of Hazardous Wastes and Their Disposal, Twelfth meeting,, UNEP , 11 May 2015.
Remediation of contaminated sites

## Slide 6
<number>
Mercury is also readily detectable using a combination of field instruments and laboratory analysis
The first priority is to isolate the contamination from the receptors as far as possible in order to minimize further exposure. In this way, sites contaminated with mercury are similar to a site with another potentially mobile, toxic contaminant.
244. If the site is residential and relatively small, ample guidance for emergency response is available from the United States EPA in their Mercury Response Guidebook, which was designed to address small- to medium-sized spills in residences (United States EPA, 2001).
Notes: At contaminated sites the surface and sub-soil, sediment, surface and ground water may need to be adequately treated. A number of processes are available for on– and off-site treatment (see for example the EU‘s relevant Best Available Techniques Reference Document (BREFs)51 or the US EPA‘s ‘Treatment Technologies for Mercury in Soil, Waste and Water’80
<number>

## Slide 7
<number>
Treatment of Soil Contaminated with Mercury through a Combination of Wet Screening and Vacuum Distillation (France))
Notes: Mercury contaminated soil and building rubble was treated by a combination of soil washing and using a vacuum thermal desorption unit (vacuum mixer). In order to reduce the amount of material that has to be treated in the vacuum mixer, a soil washing process was utilized. Coarse material, which is generally less contaminated, was separated from fine material, which contains the bulk of the contamination, by a washing process. The fine material was sent to the vacuum mixer. Coarse material was tested and declared as cleaned solid if it met the quality criteria. If not, it was crushed and treated in the vacuum mixer.
The material treated by the vacuum mixer achieved a final mercury content of less than 1 ppm and leached less than 0.001 mg/l. After the treatment, stabilization was used to reduce the leachability of other heavy metals and the clean material was used for backfilling on-site.
<number>

## Slide 8
<number>
Combination of Wet Screening and Vacuum Distillation Flow Chart
Notes: Mercury contaminated soil and building rubble was treated by a combination of soil washing and using a vacuum thermal desorption unit (vacuum mixer). In order to reduce the amount of material that has to be treated in the vacuum mixer, a soil washing process was utilized. Coarse material, which is generally less contaminated, was separated from fine material, which contains the bulk of the contamination, by a washing process. The fine material was sent to the vacuum mixer. Coarse material was tested and declared as cleaned solid if it met the quality criteria. If not, it was crushed and treated in the vacuum mixer.
The material treated by the vacuum mixer achieved a final mercury content of less than 1 ppm and leached less than 0.001 mg/l. After the treatment, stabilization was used to reduce the leachability of other heavy metals and the clean material was used for backfilling on-site.
<number>

## Slide 9
Euro Chlor. (2009). Guideline for Decommissioning of Mercury Chlor-Alkali Plants. Environmental Protection 3, 5th Edition
US EPA. (2007). Treatment Technologies for Mercury in Soil, Waste, and Water. Available at: http://www.epa.gov/tio/download/remed/542r07003.pdf
Wang, J.; Feng, X.; Anderson, C. W. N.; Xing, Y. and Shang, L. (2012). Remediation of mercury contaminated sites – A review. Journal of Hazardous Materials, 221-222, pp. 1-18.
GRS. (2008). REMCOSITE – Remediation of Mercury Contaminated Sites. Sino-German Workshop 2008, Guiyang, May 27 – 30, 2008. Available at: http://www.grs.de/sites/default/files/pdf/Remcosite_2008_Chemieabfaelle_0.pdf.
World Bank. (2010). International Experience in Policy and Regulatory Frameworks for Brownfield Site Management. Discussion Papers. Available at: https://openknowledge.worldbank.org/bitstream/handle/10986/2927/578900ESW0P11910BOX353785B01PUBLIC1.pdf?sequence=1.
Network for Industrially Contaminated Land in Europe. (2015): Welcome to NICOLE. Available at: http://www.nicole.org/.
US EPA. (2015). Initiatives in Europe for the remediation in contaminated soil. Available at: http://www.epa.gov/oswer/international/factsheets/200906_eu_soils_contamination.htm#initiatives.
US EPA. Remedial Design/Remedial Action. Available at: http://www.epa.gov/superfund/cleanup/rdra.htm.
Federal Remediation Technologies Roundtable. (2015). Available at: http://www.frtr.gov/.
<number>
Useful references on Remediation
Notes: At contaminated sites the surface and sub-soil, sediment, surface and ground water may need to be adequately treated. A number of processes are available for on– and off-site treatment (see for example the EU‘s relevant Best Available Techniques Reference Document (BREFs)51 or the US EPA‘s ‘Treatment Technologies for Mercury in Soil, Waste and Water’80
Virgin mercury-
storage cost, disposal cost
Recovered and excess mercury –
storage, cost of clean up before sale, disposal cost
Three markets for mercury (US, EU, RoW
<number>

## Slide 10
<number>
Parties are required to ensure that mercury or mercury compounds intended for a use allowed under this Convention are stored in an environmentally sound manner, taking into account any guidelines that are available and any requirements that the Conference of Parties adopts.
Parties shall cooperate, as appropriate with each other and with relevant IGOs and other entities to enhance capacity building
the Minamata Convention: Art. 10, Paras 2,3 and 4
Article 10 Environmentally sound interim storage of mercury other than waste mercury

## Slide 11
For more information contact:
Desirée Montecillo Narvaez
Tel : +41 22 917 8865 Fax : +41 22 797 3460 E-mail: Desiree.Narvaez@unep.org
Division of Technology, Industry and Economics
Chemicals Branch
International Environment House 1
11-13 Chemin des Anémones
CH 1219 Châtelaine
Geneva, Switzerland
Or visit:
http://www.unep.org/hazardoussubstances/Mercury/tabid/434/language/en-US/Default.aspx
Thank you for your attention
<number>